Homework 1

1. The state of a Linear Feedback Shift Register from a 1-error-correcting (7,4) cyclic decoder, after the whole received word bold r , is:
left[matrix{1## 0## 1}right]

The generator polynomial is g( x )= 1 oplus x^2 oplus x^3 .

Is there an error present? If yes, find the location of the error (its position in bold r ).

2. In a multiplication circuit with 4 modulo-2 adders places outside the binary cells, we know the following:
- during the first 4 moments, the input is 1 0 0 1 and the output is 1 1 0 1
- during the first 5 moments, the last binary cells has the values 0 0 0 0 1

Find the generator polynomial of the circuit.

Hint: draw the functioning table, fill the known values, then reason what are be the values of g_i